## Slide 1
VLSI DESIGN & VERIFICATION PROJECT
AMBA APB Master-Slave
RTL Design & Verification
A fully synthesizable Verilog implementation of ARM's low-power peripheral bus protocol — from RTL design to industry-style functional verification.
Raghav | NIT Delhi — VLSI Design & Technology

## Slide 2
What is the APB Protocol?
The simplest way to think about it
Think of it like an office intercom
A manager (the Master) needs to send instructions to different departments (the Slaves) — storage, records, or reference desks.
Only one department can be spoken to at a time — clean, orderly, no confusion.
APB (Advanced Peripheral Bus) is that simple, low-power communication system inside a chip.
It's part of ARM's AMBA family — used to connect small, simple peripherals rather than high-speed memory.
Why it's used in real chips
Low Power
Ideal for peripherals that don't need constant high-speed access
Simple Logic
Fewer signals & simpler timing than high-speed AMBA buses (AXI/AHB)
Widely Used
Found in nearly every ARM-based SoC — UART, GPIO, timers, sensors

## Slide 3
Project Overview
End-to-end: RTL design, simulation, and industry-style verification
5
RTL Modules
4
Testbench Files
100%
Sim Pass Rate
100 MHz
Clock Speed
Scope of Work
Designed a Master, an Interconnect, and 3 Slave peripherals (RAM, Register file, ROM), fully synthesizable in Verilog.
Built a 4-file, reusable testbench architecture to verify protocol correctness under multiple scenarios.
Simulated using Icarus Verilog on EDA Playground — a free, browser-based Verilog simulation platform.
Produced full industry-style documentation: test plan, verification plan, bug report, and README.

## Slide 4
System Architecture
One Master, one Interconnect, three Slaves — wrapped in apb_top
APB Master
Drives PSEL/PENABLE
& transactions
APB Interconnect
Decodes address,
routes PSEL to slave
APB Slave RAM
Read/write memory,
configurable wait states
APB Slave REG
Control/status registers,
single-cycle access
APB Slave ROM
Read-only config data,
distinct wait-state timing
All modules instantiated together inside the top-level wrapper: apb_top

## Slide 5
RTL Components — What Each Module Does
APB Master
Runs the protocol state machine (IDLE → SETUP → ACCESS), generating correctly-timed control and address/data signals for every transaction.
APB Interconnect
Decodes the address bus and routes the select signal (PSEL) to the correct slave — acting as the traffic controller of the bus.
APB Slave RAM
A read/write memory block with its own address range and configurable wait states, used for general data storage.
APB Slave REG
Models typical peripheral control/status registers — tests single-cycle, fast-access style transactions.
APB Slave ROM
A read-only slave simulating fixed configuration data, with distinct timing to test how the master handles slower peripherals.
apb_top Wrapper
Integrates all 5 modules into one synthesizable top-level design, ready for simulation or synthesis.

## Slide 6
Verification Environment
A 4-file testbench architecture for structured, scalable checking
1
tb_top.v
Top-level testbench
Instantiates the DUT (apb_top) and orchestrates the overall simulation.
2
tb_tasks.v
Reusable tasks
Abstracts common read/write transactions into reusable Verilog tasks — keeps tests clean and readable.
3
test_scenarios.v
Directed test cases
Covers reads/writes across all 3 slaves, boundary addresses, and back-to-back transactions.
4
apb_protocol_checker.v
Protocol checker
Continuously monitors signals for protocol violations — catches bugs functional tests alone might miss.

## Slide 7
Catching Bugs the Right Way
Why a protocol checker matters — and what it caught
Checkers, not just tests
Note: in a pure Verilog (non-SystemVerilog) project, these are correctly called Checkers — not Assertions.
A dedicated checker module watches control signals every cycle, flagging invalid transitions in real time.
This catches subtle protocol violations that functional (input/output) tests alone can miss.
Modeled after how real verification teams separate 'does it work' from 'does it follow the rules.'
Real bugs found & fixed
Timing mismatches between wait-state slaves and master's ACCESS phase.
Address-decode edge cases at slave boundary regions in the interconnect.
Incorrect signal hold during back-to-back transactions.
Each bug was logged, root-caused, and documented in a formal bug report — not just silently patched.

## Slide 8
Key Technical Specifications
Parameter | Value | Notes
Address Width | 8 bits | Sufficient to address all 3 slave regions distinctly
Data Width | 8 bits | Matches simple peripheral register/data sizes
Clock Frequency | 100 MHz | Standard reference clock for simulation
Number of Slaves | 3 (RAM, REG, ROM) | Each at a distinct, non-overlapping address range
Wait States | Slave-specific | Deliberately varied to stress-test master/interconnect timing
Simulator | Icarus Verilog | Run on EDA Playground (browser-based, free)
Verification Style | Directed testing + protocol checker | Functional coverage + real-time rule checking
Pass Rate | 100% | All directed test scenarios passing with 0 checker violations

## Slide 9
Documentation & Deliverables
Built and documented the way a real industry team would hand it off
Test Plan
Defines what needs to be tested — all read/write scenarios, edge cases, and boundary conditions across the 3 slaves.
Verification Plan
Outlines the overall verification strategy, checker architecture, and pass/fail criteria.
Bug Report
Documents every bug found — root cause, fix applied, and how it was verified afterward.
README
A clear, structured guide to the repo: module descriptions, how to simulate, and how to interpret results.

## Slide 10
Results & Takeaways
Final Results
All directed test scenarios passed — 100% simulation pass rate
Zero unresolved protocol checker violations at project close
Multiple real RTL/timing bugs identified, root-caused, and fixed
Fully synthesizable RTL — not just simulation-only code
Skills Strengthened
RTL design fundamentals — clean, synthesizable Verilog structure
Structured verification methodology — not just 'does it pass' but 'is it proven correct'
Reusable testbench architecture design for scalability
Industry-style documentation practices for design handoff
Bug triage: root-causing, fixing, and re-verifying systematically